## Slide 1: CSE 219: Digital Logic & Computer Design
Tamanna Haque Nipa
Assistant Professor
Dept. of CSE
Stamford University Bangladesh

## Slide 2: Floating Point Number Representation
What is floating point?
= 0.5 x 10-4
= 0.125 x 10-1
= - 0.23 x 10-2
= 0.69 x 102
Basic Format:
Base will 2 or 10 depending on number system.
0.00005
0.0125
- 0.0023
69.00

## Slide 3: Basic Format
As we need to represent a float value using 0 / 1, so the base must be 2 (fixed).
So we need to store only
  M (Mantissa) and
  E (Exponent)

## Slide 4: Example
Let we are representing a 3 bit float value. That means M and E both are 3 bits.
(---, ---)
(M , E)
Here, M and E both are represented using Sign Magnitude format (integer representation)
We need to find 4 values
    Highest +ve value
    Highest –ve value
    Lowest +ve value and
    Lowest –ve value

## Slide 5: Example cont… [M and E both are 3 bits (M, E) ]
    Highest +ve value (+M, +E)
    Lowest +ve value (+M, -E)
( 011, 011) = 3 x 23 = 3 x 8 = 24
    Highest –ve value (-M, -E)
( 001, 111) = 1 x 2-3 = 1 x 1/8 = 0.125
    Lowest -ve value (-M, +E)
( 101, 111) = -1 x 2-3 = -1 x 1/8 = -0.125
( 111, 011) = -3 x 23 = -3 x 8 = -24

## Slide 6: Range – 3 bit FP
So range is
-24 to +24
All values cant be represented
The previous value of +24 is
(010, 011) = +2 x 23
=2 x 8
= 16
0
24…
… -24
0.125
-0.125
16
xxx

## Slide 7: Problems
All values cant be represented (So arithmetic operation is not possible)
0.125 to 0 there are many values
0 to -0.125 there are many values
+25 to +∞
-25 to -∞
Underflow
Overflow
Not a Number (NaN)
 Not defined
Zero representation
 too many ways

## Slide 8: Zero Representation
M must be Zero and E can be anything, 0 x 2E
If M=0, then M can be written as 2 ways
+ve zero , M= 000 and -ve zero, M = 100
As E can be anything, so using 3 bit for E, we will get 8 possible combinations. That means-
M = 000, E = 000
001
010
.
.
111
M = 100, E = 000
001
010
.
.
111
and
2 x 8 = 16 formats
If M and E are 4 bits then 2 x 16 =32 ways we can represent zero
 Not Possible

## Slide 9: Normalization and Biasing
For binary representation, before point will be 0 and after point the first value must be 1.
0.1bbbbb x 2E [Here, b can be 0 or 1]
0.000005
0.0005 x 10-2
0.5 x 10-5
5.0 x 10-6
 Must be represented in 1 way
√

## Slide 10: IEEE 754 Standard
Types
1) Single Precision (float)  32 bit
2) Double Precision (double)  64 bit
S=1
E=8 bit
M=23 bit
S=1
E=11 bit
M=52 bit

## Slide 11: Example (32 bit)
Represent 78.325
If the value is +ve then S=0 otherwise S=1
To get1.M, the given value must be divided by immediate smaller power of 2.
2 4 8 16 32 64 128 256 512 …..
78.325

## Slide 12: Example (32 bit)cont…
64
26
2E-127=6
Here, E-127=6
» E = 6+127
» E = 133
Excess 127
(Biasing Exponent)

## Slide 13: Example (32 bit)cont…
E = 133 
0
10000101
M=23 bit
1
0
0
0
0
1
0
1
+128 64 32 16 8 4 2 1
133-128=5
5-4=1
We got,
We have 1.M = 1 is in equation. So it not required to store. We need to covert M into binary value.

## Slide 14: Example (32 bit)cont…
M =
Multiply | Result | Integer Part
0.223828 x 2 | 0.447656 | 0
0.447656 x 2 | 0.895312 | 0
0.895312 x 2 | 1.790624 | 1
0.790624 x 2 | 1.581248 | 1
0.581248 x 2 | 1.162496 | 1
… | … | ….
upto 23 bits
00111…
(we will calculate 5/6 bit positions)

## Slide 15: Example (32 bit)cont…
Represent -78.325
0
10000101
00111….
We got, 78.325 =
1
10000101
00111….

## Slide 16: Set Interpretations (32 bit)
If E = 255 and M≠0 then NaN
If E = 255 and M= 0 then ±∞ (overflow)
If E = 0 and M= 0 then zero (0)
If 0<E < 255 and M≠0 then
(Underflow)
If E = 0 and M≠0 then

## Slide 17: Exercise
Represent -1.5
Solve Yourself.
Thank You.