## Slide 1: CSE 219: Digital Logic & Computer Design
Tamanna Haque Nipa
Assistant Professor
Dept. of CSE
Stamford University Bangladesh

## Slide 2: Memory Address Decoding
Address decoding refers to the way a computer system decodes the addresses on the address bus to select memory locations in one or more memory or peripheral devices.

## Slide 3: PIPO – 4 bit
CLK
IN/OUT

## Slide 4: Address Decoder (4 x 8)
8 bit
0
1
2
3
2 x 4 line decoder
A1
A0

## Slide 5: Address Decoder (4 x 8)

## Slide 6: Address Decoder (4 x 8)
4 x 8 RAM / ROM
A1
A0

## Slide 7: Address Decoder
Address A1 and A0 (2 bit) then addressable memory 22= 4
Address A0 to A9 (10 bit) then addressable memory 210 = 1024 (1 K)
Address A0 to A10 (11 bit) then addressable memory 211 = 2048 (2 K)

## Slide 8
E1 0V +5V
CS
3 to 8 decoder
ROM
8kX8
RAM
1kX8
A15
A14
A13
A12
A0
A9
A0
RD WR
O3
O6
CS
RD
A19
A18
A17
A16
1st Address:
A19 A18 A17 A16 A15 A14 A13 A12 A11 A10 A9 A8 A7 A6 A5 A4 A3 A2 A1 A0
0
110
Last Address:
A19 A18 A17 A16 A15 A14 A13 A12 A11 A10 A9 A8 A7 A6 A5 A4 A3 A2 A1 A0
1 1 0 1 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1
Address of ROM:
DC000
DDFFF
1 1 0 1
0 0 0 0 0 0 0 0 0 0 0 0 0
1 1 0

## Slide 9
E1 0V +5V
CS
3 to 8 decoder
ROM
8kX8
RAM
1kX8
A15
A14
A13
A12
A0
A9
A0
RD WR
O3
O6
CS
RD
A19
A18
A17
A16
1st Address: D6000
A19 A18 A17 A16 A15 A14 A13 A12 A11 A10 A9 A8 A7 A6 A5 A4 A3 A2 A1 A0
1 1 0 1 0 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0
0
011
Last Address: D63FF
A19 A18 A17 A16 A15 A14 A13 A12 A11 A10 A9 A8 A7 A6 A5 A4 A3 A2 A1 A0
1 1 0 1 0 1 1 0 0 0 1 1 1 1 1 1 1 1 1 1
Address of RAM:

## Slide 10: Memory Allocation
Memory allocation is a process by which computer programs are assigned memory or space.
Types
  Non-Preemptive
    First Fit
    Best Fit
    Worst Fit
  Preemptive
    First In First Out (FIFO)
    Least Recently Used(LRU)
    Optimal(OPT)

## Slide 11: Non-Preemptive-Example
There are 5 process P1 to P5. P1, P2 and P3 has been already allocated and P4 and P5 need to allocated following the 3 algorithms. Find which one is best?
Process | Size (kb) | Address
P1 | 150 | 0
P2 | 400 | 300
P3 | 100 | 900
P4 | 150 | 
P5 | 200 | 
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
FS1 = 150 kb
FS2 = 200 kb
FS3 = 24 kb

## Slide 12: First Fit-Example
Need to fit P4=150 kb and P5= 200kb
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
Select FS1(150 kb) / FS2(200kb) / FS3(24kb) for P4= 150kb???
It will select FS1 then P5 will adjust with FS2
P4= 150 kb
P5 = 200 kb
Choose the first adjustable option

## Slide 13: First Fit-Example
Need to fit P4=150 kb and P5= 200kb
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
Select FS1(150 kb) / FS2(200kb) / FS3(24kb) for P4= 150kb???
It will select FS1 then P5 will adjust with FS2
P4= 150 kb
Choose the first adjustable option
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
FS1 = 200 kb
FS2 = 150 kb
FS3 = 24 kb

## Slide 14: Best Fit-Example
Need to fit P4=150 kb and P5= 200kb
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
Select FS1(150 kb) / FS2(200kb) / FS3(24kb) for P4= 150kb???
It will select FS1 then P5 will adjust with FS2
P4= 150 kb
P5 = 200 kb
Choose the best adjustable option

## Slide 15: Best Fit-Example
Need to fit P4=150 kb and P5= 200kb
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
Select FS1(150 kb) / FS2(200kb) / FS3(24kb) for P4= 150kb???
It will select FS2 for P4 and then P5 will adjust with FS2
P5= 200 kb
Choose the best adjustable option
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
FS1 = 200 kb
FS2 = 150 kb
FS3 = 24 kb
P4=150 kb

## Slide 16: Worst Fit-Example
Need to fit P4=150 kb and P5= 200kb
0
1024
P1 = 150 kb
149
300
P2 = 400 kb
P3 = 100 kb
700
900
1000
Select FS1(150 kb) / FS2(200kb) / FS3(24kb) for P4= 150kb???
P4 will select FS2 then P5 need to wait.
P4 = 150 kb
Choose the highest free space adjustable option

## Slide 17: Preemptive Allocation-Example
Consider the following page address traces generated by CPU with 3 available frames. Find out the action generated for FIFO, LRU and OPT replacement policies. Which algorithm is best?
1, 3, 1, 4, 7, 4, 5, 3, 2, 1, 2, 1, 3, 4, 6, 7

## Slide 18: FIFO
1 3 1 4 7 4 5 3
2 1 2 1 3 4 6 7
1
1
1
3
3
3
4
1
3
4
7
3
4
7
5
4
7
5
3
7
*
*
7
4
6
1
4
6
1
4
2
1
3
1
3
2
1
3
2
1
3
2
5
3
2
*
*
*
2
 hit =5

## Slide 19: LRU
1 3 1 4 7 4 5 3
2 1 2 1 3 4 6 7
1
1
1
3
3
3
4
1
7
4
1
7
4
1
7
4
5
3
4
5
*
*
6
4
7
6
4
3
1
4
3
1
2
1
2
3
1
2
3
1
2
3
5
2
3
*
*
*
3
 hit =5

## Slide 20: OPT
1 3 1 4 7 4 5 3
2 1 2 1 3 4 6 7
1
1
1
3
3
3
4
1
3
4
7
3
4
7
3
4
5
3
4
5
*
*
3
1
7
3
1
6
3
1
4
3
1
3
1
2
3
1
2
3
1
2
3
4
2
*
*
*
2
 hit =6
*