## Slide 1
Tamanna Haque Nipa
Assistant Professor
Dept. of CSE
Stamford University Bangladesh
CSE 219: Digital Logic & Computer Design

## Slide 2: Half-Adder
Two inputs A & B
Two outputs Cout & Sum
A | B | Cout | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1 0
A0B
AB0
Equations:
Sum= A0B +AB0 = A ⊕ B
AB
Cout= AB
A
B
Cout
Sum

## Slide 3: Full-Adder
Three inputs A, B & Cin
Two outputs Cout & Sum
A | B | Cin
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Cout | Sum
0 | 0
0 | 1
0 | 1
1 | 0
0 | 1
1 | 0
1 | 0
1 | 1
A 0
B 0
Cin 1
1
A 0
B 1
Cin 1
1 0
A 1
B 1
Cin 1
1 1

## Slide 4: Full-Adder
A | B | Cin | Cout | Sum
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
A0B0Cin
A0BC0in
AB0C0in
ABCin
Sum = A0B0Cin + A0BC0in + AB0C0in + ABCin
ABCin
ABC0in
AB0Cin
A0BCin
Cout = A0BCin + AB0Cin + ABC0in + ABCin

## Slide 5: Full-Adder
Sum = A ⊕ (B ⊕ Cin)
Cout = Cin(A ⊕ B) + AB
= (A ⊕ B )⊕ Cin
A
B
Cin
Cout
Sum

## Slide 6: 4 bit Parallel Adder
Full Adder
A
B
Sum
Cin
Cout
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin =0
Cout

## Slide 7: 4 bit Parallel Adder
FA 0
A0
B0
S0
Cin = 0
Cout
FA 1
A1
B1
S1
FA 2
A2
B2
S2
FA 3
A3
B3
S3

## Slide 8: 4 bit Parallel Adder
FA 0
A0
B0
S0
Cin = 0
Cout
FA 1
A1
B1
S1
FA 2
A2
B2
S2
FA 3
A3
B3
S3

## Slide 9: 4 bit Parallel Adder (Ripple Adder)
4 bit Full Adder
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin = 0
Cout
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin =0
Cout
0 1 0 1 = 5
0 1 1 1 = 7
1 1 0 0 = 12
Cin =0
Cout = 0
1
1
1

## Slide 10: Half-Subtractor
Two inputs A & B
Two outputs Bin & Difference
A | B | Bin | Diff
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
A0B
AB0
A0B
A

## Slide 11: Full-Subtractor
Three inputs A, B & Bout (Borrow out)
Two outputs Bin (Borrow in) & Difference
A | B | Bout
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Bin | Diff
0 | 0
1 | 1
1 | 1
1 | 0
A 0
B 0
Bout 1
1
A 0
B 1
Bout 0
1 1
A 0
B 1
Bout 1
1 0
+
8 3
1 5
+10
8
1+
6
1

## Slide 12: Full-Subtractor
Three inputs A, B & Bout (Borrow out)
Two outputs Bin (Borrow in) & Difference
A | B | Bout
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Bin | Diff
0 | 0
1 | 1
1 | 1
1 | 0
0 | 1
0 | 0
0 | 0
1 | 1
A 1
B 0
Bout 0
0 1
A 1
B 0
Bout 1
0 0
A 1
B 1
Bout 1
1 1
8 3
1 5
+10
8
1+
6
2
+2

## Slide 13: Full-Subtractor
A | B | Bout | Bin | Diff
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
A0B0Bout
A0BB0out
AB0B0out
ABBout
Diff = A0B0Bout + A0BB0out + AB0B0out + ABBout
ABBout
A0BBout
A0BB0out
A0B0Bout
Bin = A0B0Bout + A0BB0out + A0BBout + ABBout

## Slide 14: Full-Subtractor
Diff = A ⊕ (B ⊕ Bout)
A
B
Bout
Bin
Diff
Bin= A0(B ⊕ Bout) + BBout

## Slide 15: adder-subtractor
Subtraction: F = A-B = A + (-B) = A + B0 + 1
Example: -9
9 = 1001 X
9 = 01001 – 5 bit
Negative values are represented by 2’s complement method
2 Steps: a) 1’s complement of 9 --- 10110 = (9)0
b) add 1 with it --- 10111 (-9)
-B = B0 + 1
-8 | 4 | 2 | 1
1 | 0 | 0 | 1
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 0 | 1
= 8+1 = 9
= -8+1 = -7

## Slide 16: adder-subtractor
Addition: F = A + B
Subtraction: F = A-B = A + (-B) = A + B0 + 1
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin =0
Cout
0 1 0 1 = 5
0 1 1 1 = 7
1 1 0 0 = 12
Cin =0
Cout = 0
1
1
1
A3 A2 A1 A0
(B3 B2 B1 B0)0
S3 S2 S1 S0
Cin =1
Cout
0 1 0 1 = 5
1 0 0 0 = (7)0
1 1 1 0 = -2
Cin =1
Cout = 0
1
0
0

## Slide 17: adder-subtractor Circuit
How to implement B0 ?
0 1 1 1 = 7
1 1 1 1
1 0 0 0 = (7)0
XOR with 1
A | B | F=A⊕B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 1 1 1 = 7
0 0 0 0
XOR with 0
0 1 1 1 = 7

## Slide 18: adder-subtractor Circuit
4 bit Full Adder
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin = 0
Cout = 0
For Add Cin=0
0101
0111
0111 + 0101 + 0
1100
0111

## Slide 19: adder-subtractor Circuit
4 bit Full Adder
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin = 1
Cout = 0
For Subtraction Cin=1
0101
0111
1000 + 0101 + 1
1110
1000