## Slide 1: CSE 219: Digital Logic & Computer Design
Tamanna Haque Nipa
Assistant Professor
Dept. of CSE
Stamford University Bangladesh

## Slide 2: Integer Representations
Unsigned Integer
Signed Integer
  Sign Magnitude
  1’s Complement
  2’s Complement

## Slide 3: Number Representation (8 bit)
Positive Number Representation:
2’s complement +ve number : represent 87
87 is greater than +64 and lower than +127
87-64= 23
23-32 = x
23-16=7
7-8=x
7-4=3
3-2=1
1-1=0
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
87 = 64+16+4+2+1

## Slide 4: Number Representation (8 bit)
Positive Number Representation: represent 87
2’s complement +ve number : 87 = 01010111
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Sign Magnitude: 87 = 01010111
(87 = 64+16+4+2+1)
1’s complement: 87 = 01010111
Same as 2’s complement

## Slide 5: Number Representation (8 bit) cont…
Negative Number Representation:
2’s complement -ve number : represent -87
-87 = -128 + 41
41-64=x
41-32=9
9-16=x
9-8=1
1-4=x
1-2=x
1-1=0
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
-87 = -128+ 41
= -128 +32+8+1

## Slide 6: Number Representation (8 bit)
Negative Number Representation: represent -87
2’s complement -ve number : -87 = 10101001
Sign Magnitude: 87 = 01010111, So -87 will be 11010111
1’s complement: 87 = 01010111, So -87 will be 10101000
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
-87 = -128+ 41
= -128 +32+8+1
87 | + ve | ve
SM | 01010111 | 11010111
1’s | 01010111 | 10101000
2’s | 01010111 | 10101001

## Slide 7: Sign Magnitude
Advantages: Simple
Disadvantages:
  Zero Representation (Zero always positive)
    +ve zero 0000
    - ve zero 1000
  Problems in Arithmetic Operation
    5 +(-5)=5-5=0
    0101 = +5 and 1101 = -5
  (0101 + 1101) = 1 0010 ….. Wrong answer
  Extra circuit is required to calculate the sign bit
0101 = 5, 1010 = -2 here n = 4 bit
(5+(-2)) = (0101 + 1010) = S111, here S=0/1 need to decide.

## Slide 8: 1’s Complement
Disadvantages:
  Zero Representation (Zero always positive)
    +ve zero 0000
    - ve zero 1111
  Problems in Arithmetic Operation, Error correction is required
    5 +(-5)=5-5=0
    0101 = +5 and 1010 = -5
  (0101 + 1101) = 1111….. Wrong answer as it represents -0
  If we need to correct it, we will add 1.
  (1111 + 1) = 1 0000, here we will not consider the carry bit so the
  result will be +0.

## Slide 9: 2’s Complement
Disadvantages: Complex
Advantages:
  Zero Representation (Zero always positive)
    +ve zero 0000
    - ve zero 1111 +1 =1 0000
  No problems in Arithmetic Operation and no error correction is required
    5 +(-5)=5-5=0
    0101 = +5 and 1011 = -5
  (0101 + 1011) = 1 0000 …. Need to discard the carry bit only
  No extra circuit is required to calculate the sign bit
Zero = 0000

## Slide 10: Range: 8 bit (-ve to +ve)
Highest +ve number within 8 bit: 64+32+16+8+4+2+1 = +127
Highest -ve number within 8 bit:
-128+0=-128
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 11: Bit Extension
Positive Value : 30 =011110 (2’s complement)
30 | 6 bit | 9 bit
SM | 011110 | 000011110
1’s | 011110 | 000011110
2’s | 011110 | 000011110
Negative Value: -30 =100010 (2’s complement)
30 | bit | 9 bit
SM | 111110 | 100011110
1’s | 100001 | 111100001
2’s | 100010 | 111100010

## Slide 12: Binary Codes
In the coding, when numbers, letters or words are represented by a specific group of symbols, it is said that the number, letter or word is being encoded. The group of symbols is called as a code. The digital data is represented, stored and transmitted as group of binary bits. This group is also called as binary code.
Advantages of Binary Code
  Suitable for the computer applications.
  Suitable for the digital communications.
  Make the analysis and designing of digital circuits
  Since only 0 & 1 are being used, implementation becomes easy.

## Slide 13: Classification of binary codes
The codes are broadly categorized into following four categories.
On the basis of weight
  Weighted Codes
  Non-Weighted Codes
    Excess-3 code
    Gray Code
Binary Coded Decimal Code
Alphanumeric Codes
Error Codes
  Error Detecting Codes
  Error Correcting Codes

## Slide 14: Binary Coded Decimal (BCD) code
In this code each decimal digit is represented by a 4-bit binary number. BCD is a way to express each of the decimal digits with a binary code. With four bits we can represent sixteen numbers (0000 to 1111). But in BCD code only first ten of these are used (0000 to 1001). The remaining six code combinations i.e. 1010 to 1111 are invalid in BCD.

## Slide 15: Excess-3 code (XS-3)
The Excess-3 code words are derived from the 8421 BCD code words adding (0011)2 or (3)10 to each code word in 8421.
Exercise: Find Excess-5 code.
CAT
ECV

## Slide 16: Gray Code (Cyclic Code, Reflected Binary Code (RBC), Reflected Binary (RB) or Grey code)
It has a very special feature that, only one bit will change each time the decimal number is incremented. As only one bit changes at a time, the gray code is called as a unit distance code. Gray code cannot be used for arithmetic operation.

## Slide 17: Gray Code

## Slide 18: Code Conversion - Binary to Gray (3 bit)
Binary Code |  | 
A | B | C
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Gray Code |  | 
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 1
0 | 1 | 0
1 | 1 | 0
1 | 1 | 1
1 | 0 | 1
1 | 0 | 0
Equation
Truth Table:
X=AB0C0 +AB0C + ABC0 +ABC
=AB0(C0 + C) + AB(C0 + C)
=AB0 + AB
=A(B0 + B) =A
Y=A0BC0 +A0BC + AB0C0 +AB0C
=A0B(C0 + C) + AB0(C0 + C)
=A0B + AB0
=A ⊕ B
Z=A0B0C + A0BC0 +AB0C + ABC0
=A0B0C +AB0C + A0BC0 + ABC0
= B0C(A0 +A) + BC0 (A0+ A)
= B0C + BC0
= B ⊕ C

## Slide 19: Code Conversion - Binary to Gray (3 bit)
Binary Code |  | 
A | B | C
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Gray Code |  | 
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 1
0 | 1 | 0
1 | 1 | 0
1 | 1 | 1
1 | 0 | 1
1 | 0 | 0
Equation
Truth Table:
X=A
Y=A ⊕ B
Z= B ⊕ C
A
B
C
X
Y
Z

## Slide 20: Code Conversion – Gray to Binary (3 bit)
Binary Code |  | 
A | B | C
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Gray Code |  | 
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 1
0 | 1 | 0
1 | 1 | 0
1 | 1 | 1
1 | 0 | 1
1 | 0 | 0
Equation
Truth Table:
A=XYZ0 +XYZ + XY0Z +X0YZ
=XY(Z0 + Z) + Z(XY0 + X0Y)
=XY + Z(X ⊕ Y)
B=X0YZ +X0YZ0 + XYZ +X0YZ
=X0Y(Z + Z0 ) + YZ (X+X0)
=X0Y + YZ = Y(X0+Z)
C=X0Y0Z +X0YZ0 + XYZ +X0YZ
=X0(Y0Z +YZ0) + YZ (X+X0)
=X0(Y ⊕ Z) + YZ

## Slide 21: Code Conversion – Gray to Binary (3 bit)
Binary Code |  | 
A | B | C
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Gray Code |  | 
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 1
0 | 1 | 0
1 | 1 | 0
1 | 1 | 1
1 | 0 | 1
1 | 0 | 0
Equation
Truth Table:
A=XY + Z(X ⊕ Y)
B= Y(X0+Z)
C =X0(Y ⊕ Z) + YZ
X
Y
Z
X
Z
Y

## Slide 22: Code Conversion - Binary to Excess-3 (3 bit)
Binary Code |  | 
A | B | C
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
 | Excess-3 Code |  | 
W | X | Y | Z
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
Equation and Diagram
Do Yourself

## Slide 23: Code Conversion
Excess-3 to Binary
BCD to Gray
BCD to Excess-3
Gray to BCD
Excess-3 to BCD