## Slide 1: CSE 219: Digital Logic & Computer Design
Tamanna Haque Nipa
Assistant Professor
Dept. of CSE
Stamford University Bangladesh

## Slide 2: Decoders
A decoder is a digital circuit that detects the presence of a specified combination of bits (code) on its inputs and indicates the presence of that code by a specified output level.
In its general form, a decoder has n input lines to handle n bits and from one to 2n output lines to indicate the presence of one or more n-bit combinations.
2 to 4 Line
Decoder
A
B
D0
D1
D2
D3

## Slide 3: 2 to 4 Line Decoder
Equations:
D0 = A0B0
D1 = A0B
D2 = AB0
D3 = AB
A | B
0 | 0
0 | 1
1 | 0
1 | 1
D0 | D1 | D2 | D3
1 | 0 | 0 | 0
2 to 4 Line
Decoder
A
B
D0
D1
D2
D3
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
A
B
D0
D1
D2
D3

## Slide 4: 3 to 8 Line Decoder
D0 = x0y0z0
D1 = x0y0z
D2 = x0yz0
D3 = x0yz
D4 = xy0z0
D5 = xy0z
D6 = xyz0
D7 = xyz

## Slide 5: 3 to 8 Line Decoder
D0 = x0y0z0
D1 = x0y0z
D2 = x0yz0
D3 = x0yz
D4 = xy0z0
D5 = xy0z
D6 = xyz0
D7 = xyz

## Slide 6: 4 to 16 Line Decoder
2 to 4 line decoder ---- 2 inputs and 22 =4 outputs
3 to 8 line decoder ---- 3 inputs and 23 =8 outputs
4 to 16 line decoder ---- 4 inputs and 24 =16 outputs
5 to ? line decoder ---- 5 inputs and ? Outputs
Read yourself: Applications of Decoder

## Slide 7: 3x8 line decoder constructed with 2x4 line decoders
2 to 4 Line
Decoder
B
C
D0
D1
D2
D3
2 to 4 Line
Decoder
D4
D5
D6
D7
A
E
E
Enables if A=0
Enables if A=1
2x4 line decoder : inputs : 2, output : 4
3x8 line decoder : inputs : 3, output : 8
B | C
0 | 0
0 | 1
1 | 0
1 | 1
0 | 0
0 | 1
1 | 0
1 | 1
A
0
0
0
0
1
1
1
1

## Slide 8: 3x8 line decoder constructed with 2x4 line decoders
2 to 4 Line
Decoder
B
C
D0
D1
D2
D3
2 to 4 Line
Decoder
D4
D5
D6
D7
A
E0
E0
Enables if A=1
Enables if A=0
2x4 line decoder : inputs : 2, output : 4
3x8 line decoder : inputs : 3, output : 8

## Slide 9: 4x16 line decoder constructed with 3x8 line decoders

## Slide 10: Implementation of function using Decoder
F(X,Y,Z) = Σ (2,4,6,7)
3 to 8 Line Decoder
X
Y
Z
D0
D1
D2
D3
D4
D5
D6
D7
F

## Slide 11: Implementation of Adder using Decoder
Any Expression can be implemented by decoder
(practice: d(p,q,r,s)= Σ (0, 3, 5, 6, 7, 9, 12) )

## Slide 12: Encoder
An encoder is a digital circuit that performs the inverse operation of a decoder.
An encoder has 2n input lines and n output lines.
The output lines, as an aggregate, generate the binary code corresponding to the input value.
4 to 2 line Encoder
A
B
D0
D1
D2
D3

## Slide 13: 4 to 2 line Encoder
D0 | D1 | D2 | D3
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
A | B
0 | 0
0 | 1
1 | 0
1 | 1
A= D2+D3
B=D1+D3
D1 D2 D3
A
B

## Slide 14: 8 to 3 line Encoder

## Slide 15: 8 to 3 line Encoder
D1 D2 D3 D4 D5 D6 D7
x
y
z

## Slide 16: Encoder
4 to 2 line encoder ---- 4 inputs and 22 = 4, 2 outputs
8 to 3 line encoder ---- 8 inputs and 23 =8, 3 outputs
16 to ? line encoder --16 inputs and 24 =16, ? outputs
32 to ? line encoder ----32 inputs and ? Outputs
Read yourself: Applications of Encoder
Priority Encoder: A priority encoder is an encoder circuit that includes the priority function. The operation of the priority encoder is such that if two or more inputs are equal to 1 at the same time, the input having the highest priority will take precedence.

## Slide 17: Multiplexer
A multiplexer is a combinational circuit that selects binary information from one of many input lines and directs it to a single output line.
The selection of a particular input line is controlled by a set of selection lines.
Normally, there are 2n input lines and n selection lines whose bit combinations determine which input is selected.
2 to 1 line MUX
Y
I0
I1
S0
4 to 1 line MUX
Y
I0
I1
I2
I3
S0
S1

## Slide 18: 4 to 1 Line Multiplexer
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
Y= S10S00I0 + S10S0I1 + S1S00 I2+ S1S0I3
S1
S0
Y
I0
I1
I2
I3
4 to 1 line MUX
Y
I0
I1
I2
I3
S0
S1

## Slide 19: Multiplexer
Implement 2 to 1 line MUX
Implement 8 to 1 line MUX
Applications of MUX
Read yourself

## Slide 20: 4x1 line MUX constructed with 2x1 line MUX
2 to 1 line MUX
I0
I1
S1
2 to 1 line MUX
I2
I3
E
E
S0
2x1 line MUX : inputs : 2, selector : 1
4x1 line MUX : inputs : 4, selector : 2
Y

## Slide 21: Boolean Function Implementation
F(A,B,C,D) = Σ (2,4,6,7,10,11,14,15) … use 16x1 line MUX
16 x 1 line
MUX
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
1
0
F
A
B
C
D

## Slide 22: Boolean Function Implementation
F(A,B,C,D) = Σ (2,4,6,7,10,11,14,15) using 8x1 line MUX
16x1 line MUX : inputs : 16, selector : 4
8x1 line MUX : inputs : 8, selector : 3
 | I0 | I1 | I2 | I3 | I4 | I5 | I6 | I7
A0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
A | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Equations:
A0 :
A :
GND :
VCC :
I4
I3
I0, I1, I5
I2, I6, I7

## Slide 23: Boolean Function Implementation
F(A,B,C,D) = Σ (2,4,6,7,10,11,14,15) using 8x1 line MUX
Equations:
A0 :
A :
GND :
VCC :
I4
I3
I0, I1, I5
I2, I6, I7
8 x 1 line
MUX
0
1
2
3
4
5
6
7
F
B C D
A
0
1
Implement F(x,y,z)= Σ(0,1,4,6) using a 8x1 line MUX
Implement F(x,y,z)= Σ(0,1,4,6) using a 4x1 line MUX

## Slide 24: Implement F(x,y,z)= Σ(0,1,4,6) using a 8x1 line MUX
8 x 1 line
MUX
0
1
2
3
4
5
6
7
X Y Z
VCC
GND

## Slide 25: Implement F(x,y,z)= Σ(0,1,4,6) using a 4x1 line MUX
 | I0 | I1 | I2 | I3
X0 | 0 | 1 | 2 | 3
X | 4 | 5 | 6 | 7
Equations:
X0 :
X :
GND :
VCC :
I1
I2
I3
I0
4 x 1 line
MUX
0
1
2
3
F
Y Z
X
0
1

## Slide 26: DeMultiplexers (DeMUX)
A DeMultiplexer is a combinational circuit that directs the single input line to selected one of many output lines.
The selection of a particular output line is controlled by a set of selection lines.
Normally, there are 2n output lines and n selection lines whose bit combinations determine which output is selected.
1 to 4 Line
DeMUX
Y
O0
O1
O2
O3
S1 S0

## Slide 27: 1x4 line DeMultiplexers
I | S1 | S0 | Output
1 | 0 | 0 | O0
1 | 0 | 1 | O1
1 | 1 | 0 | O2
1 | 1 | 1 | O3
0 | X | X | 0
O0 = IS10S00
O1 = IS10S0
O3 = IS1S0
O2 = IS1S00