## Slide 1
Tamanna Haque Nipa
Assistant Professor
Dept. of CSE
Stamford University Bangladesh
CSE 219: Digital Logic & Computer Design

## Slide 2: Half-Adder
Two inputs A & B
Two outputs Cout & Sum
A | B | Cout | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1 0
A0B
AB0
Equations:
Sum= A0B +AB0 = A ⊕ B
AB
Cout= AB
A
B
Cout
Sum

## Slide 3: Full-Adder
Three inputs A, B & Cin
Two outputs Cout & Sum
A | B | Cin
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Cout | Sum
0 | 0
0 | 1
0 | 1
1 | 0
0 | 1
1 | 0
1 | 0
1 | 1
A 0
B 0
Cin 1
1
A 0
B 1
Cin 1
1 0
A 1
B 1
Cin 1
1 1

## Slide 4: Full-Adder
A | B | Cin | Cout | Sum
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
A0B0Cin
A0BC0in
AB0C0in
ABCin
Sum = A0B0Cin + A0BC0in + AB0C0in + ABCin
ABCin
ABC0in
AB0Cin
A0BCin
Cout = A0BCin + AB0Cin + ABC0in + ABCin

## Slide 5: Full-Adder
Sum = A0B0Cin + A0BCin0 + AB0Cin0 + ABCin
Cout = A0BCin + AB0Cin + ABC0in + ABCin
= A0(B0Cin + BC0in) + A(B0C0in + BCin)
= A0(B ⊕ Cin) + A(B ⊕ Cin)0
= A ⊕ (B ⊕ Cin)
= Cin(A0B+AB0) + AB(C0in + Cin )
= Cin(A ⊕ B) + AB

## Slide 6: Full-Adder
Sum = A ⊕ (B ⊕ Cin)
Cout = Cin(A ⊕ B) + AB
= (A ⊕ B )⊕ Cin
A
B
Cin
Cout
Sum

## Slide 7: Full-adder implementation with half-adders
Sum = (A ⊕ B ) ⊕ Cin
Cout = Cin(A ⊕ B) + AB
Full-Adder
Sum= A ⊕ B
Cout= AB
Half-Adder
Half-Adder
A
B
A⊕B
AB
Half-Adder
(A ⊕ B ) ⊕ Cin = Sum
Cin(A ⊕ B)
Cout
Cin

## Slide 8: 4 bit Parallel Adder
Full Adder
A
B
Sum
Cin
Cout
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin =0
Cout

## Slide 9: 4 bit Parallel Adder
FA 0
A0
B0
S0
Cin = 0
Cout
FA 1
A1
B1
S1
FA 2
A2
B2
S2
FA 3
A3
B3
S3

## Slide 10: 4 bit Parallel Adder
FA 0
A0
B0
S0
Cin = 0
Cout
FA 1
A1
B1
S1
FA 2
A2
B2
S2
FA 3
A3
B3
S3

## Slide 11: 4 bit Parallel Adder (Ripple Adder)
4 bit Full Adder
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin = 0
Cout
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin =0
Cout
0 1 0 1 = 5
0 1 1 1 = 7
1 1 0 0 = 12
Cin =0
Cout = 0
1
1
1

## Slide 12: Half-Subtractor
Two inputs A & B
Two outputs Bin & Difference
A | B | Bin | Diff
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
A0B
AB0
Equations:
Diff= A0B +AB0 = A ⊕ B
A0B
Bin= A0B
A
B
Bin
Diff

## Slide 13: Full-Subtractor
Three inputs A, B & Bout (Borrow out)
Two outputs Bin (Borrow in) & Difference
A | B | Bout
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Bin | Diff
0 | 0
1 | 1
1 | 1
1 | 0
A 0
B 0
Bout 1
1
A 0
B 1
Bout 0
1 1
A 0
B 1
Bout 1
1 0
+
8 3
1 5
+10
8
1+
6
1

## Slide 14: Full-Subtractor
Three inputs A, B & Bout (Borrow out)
Two outputs Bin (Borrow in) & Difference
A | B | Bout
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Bin | Diff
0 | 0
1 | 1
1 | 1
1 | 0
0 | 1
0 | 0
0 | 0
1 | 1
A 1
B 0
Bout 0
0 1
A 1
B 0
Bout 1
0 0
A 1
B 1
Bout 1
1 1
8 3
1 5
+10
8
1+
6
2
+2

## Slide 15: Full-Subtractor
A | B | Bout | Bin | Diff
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
A0B0Bout
A0BB0out
AB0B0out
ABBout
Diff = A0B0Bout + A0BB0out + AB0B0out + ABBout
ABBout
A0BBout
A0BB0out
A0B0Bout
Bin = A0B0Bout + A0BB0out + A0BBout + ABBout

## Slide 16: Full-Subtractor
= A0(B0Bout + BB0out) + A(B0B0out+BBout)
= A0(B ⊕ Bout) + A(B ⊕ Bout)0
= A ⊕ (B ⊕ Bout)
= A0(B0Bout + BB0out) + B Bout(A0 + A )
= A0(B ⊕ Bout) + B Bout
Diff = A0B0Bout + A0BB0out + AB0B0out + ABBout
Bin = A0B0Bout + A0BB0out + A0BBout + ABBout

## Slide 17: Full-Subtractor
Diff = A ⊕ (B ⊕ Bout)
A
B
Bout
Bin
Diff
Bin= A0(B ⊕ Bout) + BBout
Exercise: Full-Subtractor implementation with half-Subtractor

## Slide 18: adder-subtractor
Subtraction: F = A-B = A + (-B) = A + B0 + 1
Example: -9
9 = 1001 X
9 = 01001 – 5 bit
Negative values are represented by 2’s complement method
2 Steps: a) 1’s complement of 9 --- 10110 = (9)0
b) add 1 with it --- 10111 (-9)
-B = B0 + 1
-8 | 4 | 2 | 1
1 | 0 | 0 | 1
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 0 | 1

## Slide 19: adder-subtractor
Addition: F = A + B
Subtraction: F = A-B = A + (-B) = A + B0 + 1
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin =0
Cout
0 1 0 1 = 5
0 1 1 1 = 7
1 1 0 0 = 12
Cin =0
Cout = 0
1
1
1
A3 A2 A1 A0
(B3 B2 B1 B0)0
S3 S2 S1 S0
Cin =1
Cout
0 1 0 1 = 5
1 0 0 0 = (7)0
1 1 1 0 = -2
Cin =1
Cout = 0
1
0
0

## Slide 20: adder-subtractor Circuit
How to implement B0 ?
0 1 1 1 = 7
1 1 1 1
1 0 0 0 = (7)0
XOR with 1
A | B | F=A⊕B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 1 1 1 = 7
0 0 0 0
XOR with 0
0 1 1 1 = 7

## Slide 21: adder-subtractor Circuit
4 bit Full Adder
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin = 0
Cout = 0
For Add Cin=0
0101
0111
0111 + 0101 + 0
1100
0111

## Slide 22: adder-subtractor Circuit
4 bit Full Adder
A3 A2 A1 A0
B3 B2 B1 B0
S3 S2 S1 S0
Cin = 1
Cout = 0
For Subtraction Cin=1
0101
0111
1000 + 0101 + 1
1110
1000

## Slide 23: Decimal or BCD Adder
The BCD-Adder is used in the computers and the calculators that perform arithmetic operation directly in the decimal number system. The BCD-Adder accepts the binary-coded form of decimal numbers. The Decimal-Adder requires a minimum of nine inputs and five outputs.

## Slide 24: Decimal or BCD Adder cont…

## Slide 25: Decimal or BCD Adder cont…
From the above table, it is clear that if the produced sum is between 1 to 9, the Binary and the BCD code is the same. But for 10 to 19 decimal numbers, both the codes are different. In the above table, the binary sum combinations from 10 to 19 give invalid BCD. There are the following points that help the circuit to identify the invalid BCD.
It is obvious from the table that a correction is needed when the 'Binary Sum' has an output carry K=1.
The other six combinations from 10 to 15 need correction in which the bit on the Z8 position is 1.
In the Binary sum of 8 and 9, the bit on the Z8 position is also 1. So, the second step fails, and we need to modify it.
To distinguish these two numbers, we specify that the bit on the Z4 or Z2 position also needs to be 1 with the bit of Z8
The condition for a correction and an output carry can be expressed by the Boolean function:

## Slide 26: Decimal or BCD Adder cont…

## Slide 27: Decimal or BCD Adder cont…
3 8
+ 4 7
7 F
+ 0 6
8 5
Example:
3 8
+ 4 7
8 5
BCD Addition
Decimal Addition